## Slide 1: Simple calculator
Due: 5/1

## Slide 2: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Demo Reminder
More Details

## Slide 3: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Demo Reminder
More Details

## Slide 4: Small computer
Let’s consider a CPU:
  Eight 32-bit registers r0-r7. 256-byte memory.
In this project, you need to implement a calculator.
  Input: a list of expressions, consisting of:
    Integers
    Operators (+, -, *, /, =, &, |, ^, ++, --)
    Three initial variables x, y, z (each of which having an initial value)
    Some new variables
  Output: A list of assembly code.
The instructions of the CPU and the clock cycles of each instruction are listed in the following.

## Slide 5: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Demo Reminder
More Details

## Slide 6: Instruction Set Architecture (I)
Opcode | Operand1 | Operand2 | Meaning | Cycles
MOV | Register1 | Register2 | Move data from register2 to register1 | 10
 | Register1 | Constant | Set the value of register1 constant | 10
 | Register1 | [Addr2] | Move the data (4 bytes) in memory addressed Addr2 to register1. Note that Addr2 must be a multiple of 4. | 200
 | [Addr1] | Register2 | Move the data (4 bytes) from register2 to the memory addressed Addr1. Note that Addr1 must be a multiple of 4. | 200

## Slide 7: Instruction Set Architecture (II)
Opcode | Operand1 | Operand2 | Meaning | Cycles
ADD | Register1 | Register2 | Add the values in register1 to register2 and store the result in register1 | 10
SUB | Register1 | Register2 | Subtract the value in register2 from the value in register1, and store the result in register1. | 10
MUL | Register1 | Register2 | Multiply the values in register1 to register2 and store the result in register1 | 30
DIV | Register1 | Register2 | Divide the value in register1 by the value in register2, and store the result in register1. Note it is the integer division. | 50
EXIT | Constant |  | Stop the program with a constant signal, whose value is specified as follows. 0: exit normally 1: the expression cannot be evaluated | 20

## Slide 8: Instruction Set Architecture (III)
Opcode | Operand1 | Operand2 | Meaning | Cycles
AND | Register1 | Register2 | Binary and the values in register1 to register2 and store the result in register1 | 10
OR | Register1 | Register2 | Binary or the values in register1 to register2 and store the result in register1 | 10
XOR | Register1 | Register2 | Binary exclusive or the values in register1 to register2 and store the result in register1 | 10

## Slide 9: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Demo Reminder
More Details

## Slide 10: A complete grammar rules
The valid way to arrange the tokens
statement := ENDFILE(指EOF) | END(指\n) | expr END
expr := term expr_tail
expr_tail := ADDSUB_LOGICAL term expr_tail | NiL
term := factor term_tail
term_tail := MULDIV factor term_tail| NiL
factor := INT | ADDSUB INT |
ID | ADDSUB ID |
INCDEC ID | ID ASSIGN expr |
LPAREN expr RPAREN |
ADDSUB LPAREN expr RPAREN

## Slide 11: Binary Operators
The priority of &, |, and ^ is the same as +, and - .
&, |, ^ are the same as bitwise operators in C.
The left-hand side of an assignment (=) operator should be a variable.
Valid examples:
  x = 5
  x + y = 1
    According to the grammar, it is equal to x + (y = 1)
Invalid examples:
  5 = x
  (x + y) = 1

## Slide 12: Unary Operators
Two consecutive positive (+) or negative (-) signs should be regarded as a prefix increment/decrement operator. (e.g. ++x)
Only two consecutive (no spaces between) signs form an increment/decrement operator, e.g.
  ++x should be regarded as INC(++) x.
  + +x should be regarded as POSITIVE(+) POSITIVE(+) x.
The operand of an inc/dec operator should be a variable.
E.g. y=++5 or y=++(x+6) are both INVALID.

## Slide 13: Variables (I)
Built-in variables x, y, z have initial values.
  Initially stored in memory [0], [4], [8] respectively.
When a NEW variable appears, there are two cases:
A variable first appears in the left-hand side of an assignment operator (=):
  Valid, and it can be used in the future
  E.g. c = x + 5, aa = bb = 3 * x are both valid.
A variable first appears in the right-hand side of an assignment operator (=):
  Invalid, and you should print EXIT 1
  E.g. x = cc * 5, if cc is a new variable, it is invalid.

## Slide 14: Variables (II)
We guarantee that among all test cases, a new variable will NOT first appear in:
  Both side of an assignment operator (=)
    E.g. aa = aa + 1
  Prefix increment/decrement expression (++ or --)
    E.g. x = ++bb
Variable names will only contain char a-z and A-Z and may have different lengths.
You should store the final values of x, y, z in registers r0, r1, r2 respectively before you print EXIT 0.

## Slide 15: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Demo Reminder
More Details

## Slide 16: Example:
Input: x = z + 5
Output: (One of the possible outputs)
MOV r0, [0]
MOV r1, [4]
MOV r2, [8]
MOV r3, 5
ADD r3, r2
MOV r0, r3
EXIT 0
Read initial values from memory
Set a constant value 5 to r3
Add r3 (5) and r2 (z), and store the result to r3
Move the result from r3 to r0 (x)
Program ends

## Slide 17: Error handler
If the expression is invalid, such as
x = +3 % 5
y = (x+)
Your final output should be
EXIT 1
If the expression is invalid, no matter how many instructions you output, you should make sure your instructions contains an EXIT 1

## Slide 18: Error handler - Divide by zero
While doing division (/), if the right-hand side evaluates to zero, there are two cases:
No variable in the right-hand side:
  x = y / (1 + 2 - 3)
  This is an invalid expression.
At least one variable in the right-hand side:
  x = 0
  y = 5 / x
  This is a valid expression.

## Slide 19: Total clock cycles
Each instruction has an expected runtime:
  Specified by clock cycles (in the table)
The runtime of a program is:
  Sum of the clock cycles of all instructions.
Example: the following code has 90 clock cycles
MOV r0, 3 10 cc
MOV r1, 5 10 cc
MUL r0, r1 30 cc
MOV r1, 0 10 cc
MOV r2, 0 10 cc
EXIT 0 20 cc

## Slide 20: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Demo Reminder
More Details

## Slide 21: Contest (I)
The project has 3 parts:
Practice:
  A practice contest on OJ to verify your code.
  The practice will be available during the whole project.
Demo:
  20 test cases, basic and advanced.
  Submit your code to OJ on demo day.
Extra Bonus Contest:
  Submit your code to an extra contest on demo day.
  TAs will test the clock cycles of your generated assembly code.
  Less clock cycles is better.
  Top 15 winners will get extra credits.

## Slide 22: Contest (II)
We will create a contest on NTHUOJ on demo day.
  You can send your code repeatedly within the whole day.
There will be 20 testcases.
  Each valued 5 points, totally 100.
Also, remember to submit the same code to iLMS.
We will use a parser to check the correctness.
If you have any question about the project, feel free to ask your question on iLMS or email us.

## Slide 23: Plagiarism
Definition
  Copying someone else’s work
  Including variable renaming!
Policy
  Perfectly fine to ask questions and discuss.
  NOT acceptable to copy part or whole work. => zero points on the project
  Automatic tools will be used to catch cheaters.
TAs of the two classes will work together to eliminate plagiarisms. Do not cheat!! 

## Slide 24: Outline
Introduction
Instruction Set Architecture
Grammar
Operators and Variables
Example, Error Handling and Clock Cycles
Demo Reminder
More Details

## Slide 25: Test case restriction
Only specified variables and signs are allowed.
  Allowed: + - * / ( ) & | ^ 0-9 a-z A-Z
  Not allowed: @ # $ % … or more
  Symbols not allowed will not appear in the test cases.
The result should follow the elementary arithmetic.
  x=2+3*4, x will be 14
  x=(2+3)*4, x will be 20
A test case may contain multiple expressions
Multiple expressions are separated by “\n”.

## Slide 26: Program output restrictions
You should print all the assembly code.
Don’t just print the result of x, y, z.
Ex: y = 1
z = 0
x = y + 5
One of the possible correct result will be:
  MOV r0, 0
  MOV r1, 1
  MOV r2, 0
  ADD r0, r1
  MOV r3, 5
  ADD r0, r3
  EXIT 0

## Slide 27: Others
Don’t strive to optimize some strange expressions.
  E.g. x = ((1+1))*((((1+1+1)))) or x = -(-(-1))
We only test basic parenthesis.
  E.g. x = 2*(3+4)+5
You must deal with basic errors using EXIT 1.
  Extra or missing symbols (e.g. x = &|3 or x = y 3)
  Incorrect expression (e.g. 1 = 2 + 3 or ++y = 5)
Should be able to calculate numbers > 10.
  E.g. x = 11
Should be able to calculate long expressions.
  E.g. x = 4-x/z*33+4+20*31+10